## Slide 2: What is ROS?
The Robot Operating System (ROS) is a set of software libraries and tools that help you build robot applications. From drivers to state-of-the-art algorithms, and with powerful developer tools, ROS has what you need for your next robotics project. And it's all open source.
Feels like spaghetti

## Slide 3: Make ROS better
Added ROS Version Dependency via Github
Added ROS Message Definitions via Github
Model Fanuc Robot in ROS URDF/Rviz
Added Gripper to Fanuc Robot in URDF/Rviz
Model Kitting Demo bolt and bolt holder STL in ROS Rviz
Model Fanuc Robot with Gripper with Motoman with Gripper in ROS URDF/Rviz collaborating using extended CRCL

## Slide 4: Simpler Real-time Control Architecture
Robot with gripper
Bolt Rviz Simulation
ROS CRCL Package
Displayed with ROS rqt_graph
Simpler (for now) - no ROS moveit, joint_state_publisher does arm and gripper joint updates

## Slide 5: Added ROS Version Dependency via Github
Package | Version
actionlibmsgs | 1.11.8
catkin | 0.6.16
classloader | 0.3.1
cppcommon | 0.5.6
eigenconversions | 1.11.7
eigenstlcontainers | 0.1.4
fcl | 0.3.2
gencpp | 0.5.3
genlisp | 0.4.15
genmsg | 0.5.6
genpy | 0.5.7
geometricshapes | 0.4.3
geometrymsgs | 1.11.8
kdlparser | 1.11.8
libccd | 1.5.0
messagegeneration | 0.2.10
messageruntime | 0.4.12
Bash Script
!/bin/bash
# Sorted Package Version Information in simple HTML Table Format
# Usage ./versioninfo.bash pkgname
# Assume ROS installed and pkg compiles
pkgs=`rospack depends $1 |sort `
echo "<HTML><BODY>"
echo "<h1> " $1 " Package Version Dependencies </h1>"
echo "<TABLE>"
echo "<TR><TH>Package</TH><TH>Version</TH></TR>"
for pkg in $pkgs
do
ver=`rosversion $pkg `
echo "<TR><TD> $pkg </TD><TD> $ver </TD></TR>"
done
echo "</TABLE></BODY></HTML>"
Package Version Dependencies

## Slide 6: Added ROS Message Definitions via Github
Type | Name | Comment
uint8 | done=0 | 
uint8 | error=1 | 
uint8 | working=2 | 
stdmsgs/Header | header | 
uint32 | seq | 
Type | Name | Comment
uint8 | initCanon=1 | 
uint8 | endCanon=2 | 
uint8 | actuatejoints=3 | 
uint8 | moveto=4 | 
uint8 | dwell=5 | 
uint8 | message=6 | 
uint8 | moveThroughTo=7 | 
uint8 | setCoordinatedMotion=8 | 
uint8 | stopMotion=9 | 
nistcrcl/CrclStatusMsg
nistcrcl/CrclCommandMsg
Python Program

## Slide 7: Fanuc LRMate 20iD Robot in ROS/URDF/Rviz

## Slide 8: Added Gripper to Fanuc Robot in URDF – and Rviz for pick/place

## Slide 9: Fanuc and Robotiq URDF

## Slide 10: Added Bolt and Boltholder as STL to ROS using Rviz “Markers”

## Slide 11: Rviz Bang-bang Simulation of Bolt placement

## Slide 12: ROS URDF Macro language - Xacro
Once the basic URDF is in place, robot and gripper definitions can become a macro in Xacro (ok programming with XML not easy peasy)
Now Connect the robots in ROS Xacro/URDF
<?xml version="1.0"?>
<robot name="fanuc_lrmate200id" xmlns:xacro="http://ros.org/wiki/xacro">
<xacro:include filename="$(find fanuc_lrmate200id_support)/urdf/lrmate200id_macro.xacro"/>
<xacro:include filename="$(find fanuc_lrmate200id_support)/urdf/robotiq_c2_model_macro.xacro"/>
<xacro:include filename="$(find motoman_sia20d_support)/urdf/sia20d_macro.xacro"/>
<xacro:fanuc_lrmate200id prefix="fanuc_"/>
<xacro:robotiq_c2_model prefix="fanuc_"/>
<xacro:motoman_sia20d prefix="motoman_"/>
<xacro:robotiq_c2_model prefix="motoman_"/>
<link name="world" />
<!-- Dummy Link -->
<link name="link0" />
<joint name="world_joint" type="fixed">
<parent link="world" />
<child link="link0" />
<axis xyz="0 0 1"/>
</joint>
<!-- First Robot -->
<joint name="fanuc_joint_0" type="fixed">
<parent link="link0" />
<child link="fanuc_base_link" />
<origin xyz="0 -0.5 0" rpy="0 0 0"/>
</joint>
<!-- Second Robot -->
<joint name="motoman_joint_0" type="fixed">
<parent link="link0" />
<child link="motoman_base_link" />
<origin xyz="0 0.5 0" rpy="0 0 0"/>
</joint>

## Slide 13: Model Fanuc and Motoman Robots in ROS

## Slide 14: Fanuc and Motoman Robots Playing Checkers

## Slide 15: What is useful
Kinematics is confusing, simple modifications to tool offset can assist in orienting tool correctly
No heavy lifting - moving robots around is not hard – change of base offset pose
No safety reports
Validate motion concepts
Works for multiple robots ask Paul Stahura

## Slide 16: Future
Gomotion Jerk-based trajectory motion ROS library
Integration of vision and Mongo DB for object recognition and archiving
Collision checking
Prismatic gripper
Dynamic change of end effector issue – only Baxter handles, ROS ignores
Gazebo with physics modeling

## Slide 17: Block diagram